KME272 - Assesment 1.4

Baley Eccles - 652137

[2024-08-24 Sat 12:04]

# KME272 - Assesment 1.4
## Q3
1. Make an initial guess $(x_0,y_0,z_0,t_0)$
2. Construct the matrix $J^{(m)}$
3. Solve $J^{(m)}c^{(m)}=-f^{(m)}$ for $c^{(m)}$
   This can be done using mldivide
4. Update the guess $x^{(m+1)}=x^{(m)}+c^{(m)}$
5. Check if it has converged $\lvert \lvert f^{(m)}\rvert \rvert_{2} < 10^{-6}$
6. If not converged repeat steps 2 to 5
## Q4
Listing 1.2.1:
c = 299792.458;
pos = [ -15093, -519, -13414;
        -5681, 9216, -17053;
        -6228, 16581, -9711;
        -16728, 9532, -6110];
t = [0.069121, 0.071234, 0.070942, 0.070537];

        % Initial Guess
x = [0; 0; 0; 0];
tol = 10^-6;
i = 0;
maxit = 1000;
while true
  i = i + 1;

        % Calculate f
  f = zeros(4, 1);
  for k = 1:length(f)
    f(k) = (x(1)-pos(k,1))^2 + ...
        (x(2)-pos(k,2))^2 + ...
        (x(3)-pos(k,3))^2 - ...
        c^2*(x(4)-t(k))^2;
  end

        % Check for convergence
  if norm(f, 2) < tol
    disp(['Converged after ', num2str(i), ' iterations.']);
    break;
  end

        % Calculate J(m)
  J = zeros(4, 4);
  for k = 1:length(J)
    J(k, :) = [2*(x(1)-pos(k,1)), ...
        2*(x(2)-pos(k,2)), ...
        2*(x(3)-pos(k,3)), ...
        -2*c^2*(x(4)-t(k))];
  end

        % Solve for c(m)
  c_m = mldivide(J,-f);

        % Update guess
  x = x + c_m;

  if i > maxit
    fprintf("Max iterations reached (%i)\n", i)
    break;
  end
end

        % Print results
fprintf("Calculated position (x, y, z, t): (%.2f,%.2f,%.2f,%.2f)\n", x(1),x(2),x(3),x(4))
The code was tried with different inital guesses, the number of itterations required for convergence was typicall more than with the inital guess being 0. $x^{(0)}=0$ is a good inital guess becaues if the location of the reciver is close to $(x,y,z)=(0,0,0)$, then the Newton Raphson method will converge quickly.
## Q5
Listing 1.3.1:
x = [3438.332915,-3491.409159,4071.923288];
d = norm(x);
h = d - 6371;
fprintf("Recivers distance from the surface of the earth (km): %.4f\n", h)